## Slide 1: Physical interpretation of river memory and application to seasonal flood forecasting
Theano Iliopoulou, Christina Aguilar, Berit Arheimer, María Bermúdez, Nejc Bezak, Andrea Ficchi, Demetris Koutsoyiannis, Juraj Parajka, María José Polo, Guillaume Thirel and Alberto Montanari
This work was partially funded by the European Union Seventh Framework Programme (FP7/2007-2013) under grant agreement no. 603587, project Switch-On.
IAHS 2017 Scientific Assembly
10 – 14 JULY 2017, Port Elizabeth, South Africa
"Water and Development: scientific challenges in addressing societal issues”
W17: Stochastic hydrology: simulation and disaggregation models

## Slide 2: Defining river memory
Research assumption:
The various geophysical and hydrological processes involved in the river flow generating process exhibit persistence at several distinct timescales which propagates into the river flow behavior and manifests itself as high seasonal correlation.
Research questions:
Can higher/lower than usual river discharges be associated to a higher probability of extreme flows (floods and droughts) in the subsequent seasons?
How long do rivers ‘remember’ past flows?
What are the physical drivers behind generation of memory in river flow and how do they vary spatially?

## Slide 3: Data
224 European rivers of more than 50 years of daily flow data from Austria, Sweden, Slovenia, France, Spain and Italy.
Catchment characteristics
Climatic information
Site-specific information

## Slide 4: Overview of study
Seasonality characterization
Estimation of seasonal correlation
Analysis of physical drivers of correlation strength
Regressing correlation magnitude to catchment behaviors
Integrating river memory into seasonal flood prediction scheme
A real-world application

## Slide 5: High Flow Season vs Dry Month memory
We define two seasonal regimes:
  High Flow Seasons (HFS) as 3-month periods receiving the maximum amount of Peaks Over Threshold (Lee et al., 2015)
  Dry Months (DM) as the months receiving the minimum average flow within the year
We estimate lagged monthly correlation between:
  Maximum flow during HFS and average flows in antecedent months
  Average DM flow and average flows in antecedent months

## Slide 6: Spatial patterns of correlation magnitude
The large spatial variability of correlation magnitude along with the presence of spatial clustering imply the dependence of correlation on regional drivers.

## Slide 7: Investigating physical drivers: Overview and Challenges
Seeking relationships between correlation magnitude and physical features as dictated by our physical understanding of the behaviors of the river systems components:
        land processes (e.g. infiltration, baseflow, evapotranspiration)
        Meteorological forcing and hydroclimate
        site-specific local features
        and their various interactions
Interpretation of findings in physical terms is particularly difficult due to multiple processes’ interactions, e.g. processes having contradictory effects on correlation magnitude, scale effects, nonlinear dynamics, seasonality, spatial variability, random fluctuations of the system, and in general, due to natural complexity.

## Slide 8: Basin area
Basin size is representative of the scale of the natural system affecting river flow under the assumption that in larger scale systems the impact of the superposition of the climatological and geophysical processes affecting river flow becomes more significant and may lead to a magnified effect of the factors with positive contribution.
positive effect of the basin size in the correlation magnitude, which is more pronounced in the case of DM.

## Slide 9: Baseflow index
Baseflow index represents the amount of groundwater recharge, which is reflective of the amount of groundwater storage in the aquifer.
positive effect of BFI on both the DM and HFS correlation, more significant for the DM.

## Slide 10: Aridity index
Aridity index is calculated as the Mean Daily Flow divided by the basin size. The index is a measure of the significance of the streamflow component in the basin.
negative effect of AI on both DM and BFI correlation

## Slide 11: Topographic controls: Lakes
Information explored for 69 Swedish basins with different % of lake area coverage.
Lakes act as storage mechanisms, enhancing correlation for DM season.

## Slide 12: Topographic controls: Elevation
A DEM is examined for the Austrian catchments.
Spatial correlation patters are found to be consistent with the seasonality mechanisms in the area.
Higher altitude Austrian rivers are affected by snowmelt process, enhancing correlation, while rivers in the flatlands are more prone to drying out due to increased evapotranspiration in the summer, which destroys the correlation structure.
HFS
DM

## Slide 13: Topographic controls: Karstic formations
The majority of examined Slovenian catchments (21 out of 31 examined) are characterized by significant presence of karstic formations. Karstic catchments are known for having rapid response times and complex behaviour; e.g. initiating fast preferential groundwater flow and intermittent discharge from karstic springs.
Correlation decreases in the major presence of karst for both seasons.

## Slide 14: Hydroclimatic forcing: Mean Temperature
Temperature increases evapotranspiration leading to seasonal drying out of the rivers.
Mean Annual Temperature is negatively correlated to DM memory, whereas HFS correlation is found insensitive.

## Slide 15: Investigating correlations among variables
Presence of multicollinearity in the predictor variables examined
  We perform a step-wise selection of variables optimally summarizing the data and apply Principal Component Analysis to construct uncorrelated variables for regression
P= Annual Precipitation (spatially averaged), T=Mean Annual Temperature (spatially averaged), IDM=Index De Martonne, BA=Basin area, BFI=Baseflow Index, AI=Aridity Index
Green lines indicate positive correlation, red lines negative, width is proportional to magnitude.

## Slide 16: Principal Components Analysis
Selection of Baseflow Index, Aridity Index, Mean Annual Temperature and natural logarithm of the basin area as the summarizing variables to perform PCA
The first two Principal Components explain 70.7% of the total variance.
The PCA biplot reveals the similarities of rivers belonging to the same country.

## Slide 17: Regressing correlation magnitude
Identification of linear model regressing the DM correlation on the first three Principal Components, Adj. R2=0.58.
For HFS, the linear model failed to explain the variation in the data owing to the weakness of the causal relationships identified and the more complex behavior of HFS correlation impacted by the hydro-meteorological dynamics
Is a linear regression model efficient in predicting seasonal flow correlation based on the selected catchment descriptors?

## Slide 18: Updating the distribution of extremes
To take advantage of information captured in previous flows we employ a
data assimilation methodology presented by Aguilar et al. (2017).
A bivariate Gaussian distribution is fitted between the peak flow in the HFS NQp and the mean flow in the pre-HFS month NQm by first applying the Normal Quantile Transformation in order to make both marginal distributions Gaussian.
  From the Gaussian bivariate probability properties follows that for any observed NQm(t) = NQm(t) the probability distribution function of NQp conditioned on NQm is Gaussian, with parameters obtained as:
      μ(NQp) =ρ (NQm, NQp ) NQm and
      σ(NQp) = (1-ρ2 (NQm, NQp))0.5
Conditioning the distribution of extremes on observed events may enable one to update their distribution one season in advance and reduce uncertainty of associated estimates.

## Slide 19: A technical experiment
What if, a mean flow equal to its upper 5% sample quantile occurred in the pre-HFS month in a river with high HFS correlation?
The updated distribution shows a 6.06% increase (307.7 to 326.44 m3/s) in the flood estimate of the 200yr Return period.
Case study: Oise River in France, basin size 4320 km2, ρ1=0.54

## Slide 20: Conclusions (I)
Different drivers may impact HFS and DM correlation with the latter showing relatively greater response to baseflow indicators (BFI, basin area, snow-melt processes).
River memory is generally enhanced by presence of basin’s storage mechanisms (lakes, glaciers and snow melt, groundwater storage) yet it is primarily driven by atmospheric processes (rainfall, temperature, evapotranspiration), their climatic behavior, seasonality and persistent structure.
Presence of river memory increases the potential for short-term flow predictability. Conditioning the distribution of extremes to exploit information captured in the previous flows may be applied for various seasonal flow prediction purposes and for real time flood forecasting.

## Slide 21: References
Aguilar, C., Montanari, A., Polo, M.-J., 2016. Real time updating of the flood frequency distribution through data assimilation. Hydrol. Earth Syst. Sci. Discuss. 2016, 1–25. doi:10.5194/hess-2016-575
Lee, D., Ward, P., Block, P., 2015. Defining high-flow seasons using temporal streamflow patterns from a global model. Hydrology and Earth System Sciences 19, 4689.
O’Connell, P.E., Koutsoyiannis, D., Lins, H.F., Markonis, Y., Montanari, A., Cohn, T., 2016. The scientific legacy of Harold Edwin Hurst (1880–1978). Hydrological Sciences Journal 61, 1571–1590.