## Slide 1
New Data for Deciphering the Human Pressure on River Ecosystems
A Step Forward to Assess Global Water Emergency
Presentation given at the Gordon Research Conference Catchment Science: Interactions of Hydrology, Biology & Geochemistry
Proctor Academy – Andover (US) June 14-19, 2015
Alberto Montanari Department DICAM University of Bologna alberto.montanari@unibo.it www.albertomontanari.it

## Slide 2
Global water emergency
Increasing reciprocal pressure between water systems and society.
Floods, droughts, and water scarcity are exacerbating. Water quality is deteriorating.
What are the causes:
(1) Human pressure on water bodies;
(2) Urbanization;
(3) Inadequacy and deterioration of water resources systems;
(4) Climate change.
Identifying the role of each trigger is extremely important to identify solutions.
We need improved understanding and improved modeling.

## Slide 3
Recent flood events in Italy – Sardinia 2013 and Genoa 2014

## Slide 4
Spatial distribution of natural catastrophes from 1980 to 2012
Source: MunichRE, NatCatSERVICE
Floods are the first cause of fatalities and economic losses among natural disasters worldwide
Emergency Events Database – EM-DAT, 2013

## Slide 5
Floods are the first cause of fatalities and economic losses among natural disasters worldwide
Temporal evolution of natural catastrophes from 1980 to 2012
Source: MunichRE, NatCatSERVICE
Emergency Events Database – EM-DAT, 2013

## Slide 6
The recent occurrence of flood events across the globe has highlighted the urgent need of mitigation strategies to reduce flood risk
Sukkur in Sind province, Pakistan during the flood in August 2010
Copiapó, Northern Chile during the flood in March 2015
Haiti, during the flood in April 2015
United Nations Environment Programme, 2014

## Slide 7
Drought and water scarcity

## Slide 8
The Prague Statement of IAHS – To be approved A need for action to evolve Water Resources Systems
Recognising the human right to access to safe water and protection from water hazards of every individual as enshrined in international law,
Noting with satisfaction the current and past efforts made by governments, agencies and community groups to facilitate safe water supply, protect the environment and mitigate water hazards
For governments:
- A call for an holistic approach to identify sustainable solutions
- Actions should be planned at the local scale with a global vision
- Planning needs to be based on a sound scientific basis
For scientists:
- Need to go beyond scenario analysis, with an interdisciplinary approach
- Novel monitoring means are needed, along with a comprehensive treatment of uncertainty
- Adaptive and flexible design and management
For funding agencies:
- Enhanced funding is needed for basic and applied research
- Funding is needed for hydrological observatories to support adaptive management
- Enhanced support to educational initiatives is needed

## Slide 9
Ways forward to solve the global water emergency
Improved comprehension of the functioning of human impacted hydrological systems
New data and open access
Global scale analysis and solutions to local problems – A unified approach is needed, there are the means to promote it, the scientific community will provide the principles
A unified and cohesive action by the scientific community
An effective action by scientific associations and publishers to promote the visibility of hydrologic research

## Slide 10
Source: EARTH AT NIGHT 2012, https://earthdata.nasa.gov/labs/worldview
Nighttime lights are associated with the geographical position of the river network to locate the areas subjected to human pressure on water bodies

## Slide 11
Assessment of human pressure on water resources
Worldwide assessment of vulnerability (V) to floods using nighttime lights, without considering the evolution of flood hazard due to climate change
R = HEV where R: risk
H: hazard
E: exposure
V: vulnerability
Nighttime lights
River network
Ceola et al., 2014, GRL

## Slide 12
Nighttime lights
Time series from 1992 to 2013 (yearly average values)
Light is expressed through a Digital Number (DN) ranging from 0 (no light) to 63 (maximum luminosity), proportional to radiance
Spatial resolution: 30 arc second (0.00833°) – nearly 1 km at the equator
Spatial extension: 75° N – 65° S, 180° W-E
Nightlights as a proxy of anthropogenic presence
Human settlements and development in space and time
Image and Data processing by NOAA’s National Geophysical Data Center. DMSP collected by the US Air Force Weather Agency
Ceola et al., 2014, GRL

## Slide 13
Nighttime lights

## Slide 14
River network
Spatial resolution: 30 arc second (0.00833°) - nearly 1 km at the equator
Spatial extension: 62° N - 55° S, 138 W- 180° E
http://hydrosheds.cr.usgs.gov
Ceola et al., 2014, GRL

## Slide 15
Spatial extensions of global night-time lights (black solid line) and river network derived from HydroSHEDS (solid blue line). 2010 global nightlights are shown as an example.
Po river network (Italy): (A) identification of the study area (red rectangle); (B) satellite image (from Google Maps); (C) satellite image coupled with HydroSHEDS river network; (D) satellite image coupled with HydroSHEDS river network and 2012 night-time lights.
Worldwide nightlight data associated to the river network to quantify human pressure

## Slide 16
Worldwide nightlight data associated to the river network to quantify human pressure
3 scales of analysis
Global
Continental
National (countries with pop. > 300 k inhabitants)
175 study regions overall
Nightlight across the Nile River and Delta Region: (a) 2012 satellite image and (b) variation in nighttime light intensity in correspondence of the river network between 2012 and 1992
Ceola et al., 2014, GRL

## Slide 17
Goal 1
To test for a correlation between nightlights & economic losses due to floods (study period 1992-2012 – Ceola et al., GRL 2014)
Goal 2
To examine the temporal trends of nightlights in the proximity of the river network from 1992 to 2013 & identify human exposure enhancement (Ceola et al., WRR, submitted)

## Slide 18
The analysis shows a general increment of yearly-averaged nighttime lights from 1992 to 2012, thus revealing an increased exposure of human settlements to flood events during the last years
Results from Goal 1

## Slide 19
The proximity of population to streams & rivers is a source of major concern in the context of
flood risk
water pollution
anthropogenic use of water resources
alteration of river ecosystem dynamics
How close do we live to fluvial water bodies?
How has human proximity to rivers changed in time?
Temporal evolution of human proximity to rivers

## Slide 20
Identification of 5 distance-from-river classes
River pixel
1 pixel – distance from the river (~ 1 km)
2 pixel – distance from the river (~ 2 km)
3 pixel – distance from the river (~ 3 km)
4 pixel – distance from the river (~ 4 km)
Spatial distribution analysis: geographical vs human perspective
Constant in time
Variable in time

## Slide 21
sum of nightlights for distance class j, region x and year t
Human proximity to the river network
where:
nightlight value for pixel i, region x and year t
total sum of nightlight within region x (all distance classes are considered) for year t

## Slide 22
yearly variation of average human proximity to the river network (i.e. slope)
year
Human proximity to the river network: temporal analysis
where:
intercept
World
Europe
For the majority of countries, the average human proximity to the river network did not significantly change in time

## Slide 23
However, the nightlights, and thus the associated human presence, significantly increased worldwide from 1992 to 2013
Human distance-from-river range
How did the human presence observed in 1992, as represented by SOLTOT(x,1992), change its spatial distribution from 1992 to 2013?
=
We define:
as reference nightlight value
distance range within which the sum of nightlights equal to is settled
= 4
= 1.5
1992
2013

## Slide 24
yearly variation of human distance-from-river range (i.e. slope)
year
Human distance-from-river range: temporal analysis
where:
intercept
World
Europe
For the majority of countries, the human distance-from-river range significantly decreased from 1992 to 2013

## Slide 25
How can innovative information be used to solve technical problems?
Innovative worldwide information can be used to identify local scale problems – e.g., identification of vulnerable areas
Any available information needs to be used in design models – For instance, the temporal trend of nightlight data can be used to estimate future urban development therefore providing the means to apply non-stationary models
Finally, cost-benefit analysis should drive any identification process for the optimal solution to technical problems
(see Botto, A., D. Ganora, F. Laio, and P. Claps (2014), Uncertainty compliant design flood estimation, Water Resour. Res., 50, 4242–4253, doi:10.1002/2013WR014981. )

## Slide 26
Cost benefit analysis as a model selection criteria
Cropper, M.L., and Sahin, S. (2009) Valuing mortality and morbidity in the context of disaster risks. In: Policy Research Working Paper Series, The World Bank, http://dx.doi.org/10.1596/1813-9450-4832, http://elibrary.worldbank.org/doi/book/10.1596/1813-9450-4832
Our target is to seek solutions to technical problems.
Hydrological modeling leads to the estimation of design variables to design solutions through engineering.
Once a possible solution has been identified, a cost-benefit analysis is a necessary step to check its feasibility
a

## Slide 27
Conclusions
Global water emergency: need to stress the concept and bring it to the attention of governments and funding agencies
Global water emergency: need to bridge scales with a global analysis of local problems - Large scale hydrology is an opportunity but mind uncertainty!
New data, open access and virtual labs are the future. Let’s be proactive, to anticipate visions rather than following them
Cost-benefit analysis is a valuable support to identify a solution
Publishing in hydrology: what is the way forward to increase visibility? What actions should be taken? Will likes replace peer review? Again, we need to anticipate the evolution rather than following it

## Slide 28
www.iahs.info/pantarhei
Panta Rhei
A home for studying socio-hydrology and water emergency mitigation
www.iahs.info/pantarhei
Flood in the Po River – November 2000

## Slide 29
Acknowledgments
Serena Ceola
University of Bologna
Francesco Laio
Politecnico di Torino
This work is partially funded by the European Commission FP7 funded research project “Sharing Water-related Information to Tackle Changes in the Hydrosphere for Operational Needs” (grant agreement number 603587)

## Slide 30
Everything flows!
Thank you!