## Slide 1
Pierluigi Claps and
Paola Mazzoglio, Roberto Deidda, Giuseppe Volpini, Eliana Perucca
Updating the UPH list with recent disasters: the case of Bitti (Sardinia, 2020)

## Slide 3: Types of unsolved problems
17. What is the relative value of traditional hydrological observations vs soft data (qualitative observations from lay persons, data mining etc.), and under what conditions can we substitute space for time?
21. How can the (un)certainty in hydrological predictions be communicated to decision makers and the general public?

## Slide 4
Bitti (Nuoro, Sardinia)

## Slide 5: Rio (creek) Cuccureddu

## Slide 6
da Repubblica.it

## Slide 7: Discharge estimation
From the movie frames: | 
Road width | 6 m
Flow depth | 3 m
Flow velocity | 7 m/s
Sediment depth 2,2 m
Estimated (only water)

## Slide 8: Rational formula C = 0.92
RIO CUCCUREDDU | 
Area [km2] | 1,311
Length[km] | 1,54
Slope [-] | 0,131
Concentration time Kirpich [h] | 0,19
Concentration time Picking [h] | 0,23
Max Intensity [mm/h] | 98,6
Q Reconstructed [m3/s] | 33
‘Observed’ [m3/s] | 33
HEC-HMS CN=94

## Slide 9
Extremes within the event |  | 
d [h] | h [mm] | i [mm/h]
0,25 | 23,8 | 95,2
0,5 | 33,6 | 67,2
0,75 | 42 | 56,0
1 | 54 | 54,0
3 | 125,4 | 41,8
6 | 218 | 36,3
9 | 283,2 | 31,5
12 | 293,4 | 24,5
24 | 327,2 | 13,6

## Slide 10: Update 1 to the UPH: what is the concrete possibility to validate an estimate of the concentration time, as opposed to the lag time?
Recent advances:
Azizian (2019)
Beven (2020)

## Slide 11: Update 2 to the UPH: How to manage the variability of the runoff coefficient with T (admit C>1)?
The occurrence of C(T) > 1 is inherently related to general uncertainties of Q(T) and I(tc;T) as well as to the assumption of frequency equivalence between rainfall intensity and peak discharge.

## Slide 12: Types of unsolved problems
21. How can the (un)certainty in hydrological predictions be communicated to decision makers and the general public?

## Slide 13
3 STATISTICAL ‘WEAPONS’
Extremes within the event hobs |  | 
d [h] | h [mm] | i [mm/h]
0,25 | 23,8 | 95,2
0,5 | 33,6 | 67,2
0,75 | 42 | 56,0
1 | 54 | 54,0
3 | 125,4 | 41,8
6 | 218 | 36,3
9 | 283,2 | 31,5
12 | 293,4 | 24,5
24 | 327,2 | 13,6
T(hobs(d))

## Slide 14: 1 Regional analysis VAPI Sardegna 1998 (homogeneous regions)

## Slide 15: VAPI Sardegna 1998

## Slide 16: Diagramma di severità di evento Metodo VAPI Sardegna 1998 (versione originale)

## Slide 17: Esempio di applicazione del Metodo VAPI Sardegna 1998 per d ≥ 1 h

## Slide 18
NOME | Orune RF | Orune | Lula | Sos Canales (C.M.) | Mamone (Colonia Penale) | Osidda RF | Buddusò | Benetutti | Lodè | Osidda F.C. | Alà dei Sardi RF | Alà dei Sardi | Torpè
h 10 min |  |  |  | 8,6 |  |  |  | 10 |  |  |  | 9 | 
h 15 min | 14,6 |  | 15,1 | 11,2 | 16,7 | 9,7 | 14,6 | 15,5 | 6,9 | 16,6 | 13,3 | 16,2 | 12
h 30 min | 19,4 |  | 20,3 | 16 | 23,5 | 14 | 19,6 |  | 16,1 | 25 | 19,3 |  | 21,8
h 45 min | 21,3 |  | 28,2 |  |  | 16,7 | 30,5 |  |  | 34,5 | 19,8 |  | 26,7
h 1 h | 23,0 | 17,5 | 31,0 | 19 | 24,1 | 20,4 | 32,2 | 18,7 | 21,6 |  | 23,7 | 23,1 | 
h 3 h | 37,7 | 25,1 | 43,1 | 28,6 | 42,3 | 29,2 | 37,9 | 26,1 | 35,2 |  | 32,6 | 35,6 | 
h 6 h | 48,2 | 37,2 | 52,4 | 38,1 | 55,3 | 39,6 | 43,9 | 32,2 | 47,5 |  | 43,6 | 48,3 | 
h 12 h | 68,4 | 50,1 | 71,5 | 51,2 | 78,3 | 55,3 | 54,3 | 40,8 | 66,3 |  | 59,2 | 66,1 | 
h 24 h | 81,2 | 62,3 | 92,8 | 64,7 | 93,0 | 66,6 | 72,5 | 51,4 | 95,9 |  | 73,2 | 87,0 | 
Inserimento estremi su durate <1h (non esistenti nel database)

## Slide 19: pluviometri intorno a Bitti
Dimensioni dei pallini dipendenti dalla lunghezza della serie
Osservazioni di pioggia con serie non molto lunghe: non possibile analisi locale
Poche stazioni hanno misurato gli estremi della tempesta ‘Cleopatra’

## Slide 20: Geostatistical method (Deidda et al, 2021, regionless)

## Slide 21: geostatistical GEV
d [h] | h [mm] | [mm] | KToss | T [anni]
0,25 | 23,8 | 13,8 | 1,727256 | 18
0,5 | 33,6 | 18,1 | 1,851698 | 21
0,75 | 42 | 21,3 | 1,970374 | 25
1 | 54 | 23,9 | 2,259831 | 42
3 | 125,4 | 34,8 | 3,608377 | 373
6 | 218 | 44 | 4,952664 | 2363
9 | 283,2 | 50,5 | 5,603247 | 5314
12 | 293,4 | 55,8 | 5,262723 | 2831
24 | 327,2 | 70,6 | 4,63374 | 974
d [h] | h [mm] |  | KToss | T [anni]
0,25 | 23,8 | 13,8 | 1,727256 | 18
0,5 | 33,6 | 18,1 | 1,851698 | 21
0,75 | 42 | 21,3 | 1,970374 | 25
1 | 54 | 23,9 | 2,259831 | 42
3 | 125,4 | 34,8 | 3,608377 | 373
6 | 218 | 44 | 4,952664 | 2363
9 | 283,2 | 50,5 | 5,603247 | 5314
12 | 293,4 | 55,8 | 5,262723 | 2831
24 | 327,2 | 70,6 | 4,63374 | 974

## Slide 22: Diagramma di severità di evento Metodo GEV geostatistico (versione originale)

## Slide 23
Data limitations

## Slide 24: Pluviometri storici in zona
Fonti di dati
Estremi di precipitazione per durate inferiori all’ora
Annali Idrologici Storici (dal 1951 al 2011)
Annali Idrologici SardegnaArpa (dal 2012 al 2019)
Estremi di precipitazione per durate uguali o superiori all’ora
Dataset I2-RED (P. Mazzoglio, 2020)
Massimi annui di precipitazione
relativi a durate di 1, 3, 6, 12 e 24 ore consecutive
acquisiti nel periodo 1916-2019
Dato nazionale aggiornato al 2019 in Sardegna

## Slide 25: Dati disponibili (medie e lunghezze delle serie)
Progr. | NOME | h10 | anni | h15 | anni | h30 | anni | h45 | anni | h1 | h3 | h6 | h12 | h24 | Inizio | Fine | Anni
1 | Sos Canales (C.M.) | 8,6 | 19 | 11,3 | 21 | 16,1 | 21 |  |  | 19,0 | 28,6 | 38,1 | 51,2 | 64,7 | 1962 | 2006 | 42
2 | Osidda F.C. |  |  | 16,6 | 4 | 25,0 | 4 | 34,5 | 4 | 39,1 | 42,8 | 43,7 | 59,9 | 76,8 | 1992 | 1995 | 4
4 | Benetutti |  |  |  |  |  |  |  |  | 18,9 | 25,9 | 32,3 | 40,4 | 50,4 | 1987 | 2009 | 19
5 | Buddusò |  |  |  |  |  |  |  |  | 33,1 | 38,7 | 44,5 | 53,4 | 72,4 | 1929 | 1992 | 18
6 | Alà dei Sardi |  |  |  |  |  |  |  |  | 23,2 | 35,3 | 47,7 | 65,2 | 86,1 | 1971 | 2009 | 25
7 | Mamone (Colonia Penale) |  |  |  |  |  |  |  |  | 24,1 | 42,3 | 55,3 | 78,3 | 93,0 | 1929 | 2019 | 19
8 | Lula |  |  | 15,1 | 11 | 20,3 | 11 | 28,2 | 9 | 31,0 | 43,1 | 52,4 | 71,5 | 92,8 | 1988 | 2009 | 21
9 | Lodè |  |  |  |  |  |  |  |  | 21,6 | 35,2 | 47,5 | 66,3 | 95,9 | 1988 | 2009 | 19
10 | Orune |  |  |  |  |  |  |  |  | 17,5 | 25,1 | 37,2 | 50,1 | 62,3 | 1967 | 2009 | 17
11 | Torpè |  |  | 13,2 | 6 | 23,5 | 7 | 26,7 | 6 | 36,4 | 59,7 | 72,0 | 85,7 | 100,5 | 1988 | 2008 | 7
12 | Alà dei Sardi RF |  |  | 13,3 | 8 | 19,3 | 8 | 19,8 | 7 | 23,7 | 32,6 | 43,6 | 59,2 | 73,2 | 2010 | 2019 | 10
13 | Orune RF |  |  | 14,6 | 8 | 19,4 | 8 | 21,3 | 8 | 23,0 | 37,7 | 48,2 | 68,4 | 81,2 | 2012 | 2019 | 8
14 | Osidda RF |  |  | 9,7 | 8 | 14,0 | 7 | 16,7 | 7 | 20,4 | 29,2 | 39,6 | 55,3 | 66,6 | 2010 | 2018 | 9
Per San Giovanni – Bitti (C.ra) non sono disponibili dati storici di piogge orarie.

## Slide 26: Patched Kriging (Libertino et al. 2016, regionless, data patching)
ordinary kriging on every year
1932
1962
2006
1932
1962
2006
Maps of annual extremes (1-24 h)
core sample in the location
of interest

## Slide 27
I2-RED
Improved Italian – Rainfall Extreme Dataset
(Mazzoglio et al., 2020)
Annual maxima 1916-2019
Most recent data

## Slide 28: Patched Kriging GEV
d [h] | h [mm] | [mm] | KToss | T [anni]
0,25 | 23,8 | 10,8 | 2,202366 | 35
0,5 | 33,6 | 16,0 | 2,096363 | 28
0,75 | 42 | 20,2 | 2,080843 | 27
1 | 54 | 23,8 | 2,271618 | 39
3 | 125,4 | 36,0 | 3,48783 | 274
6 | 218 | 46,7 | 4,670317 | 1184
9 | 283,2 | 54,4 | 5,207954 | 2099
12 | 293,4 | 60,6 | 4,841523 | 1429
24 | 327,2 | 78,7 | 4,158793 | 653
d [h] | h [mm] |  | KToss | T [anni]
0,25 | 23,8 | 10,8 | 2,202366 | 35
0,5 | 33,6 | 16,0 | 2,096363 | 28
0,75 | 42 | 20,2 | 2,080843 | 27
1 | 54 | 23,8 | 2,271618 | 39
3 | 125,4 | 36,0 | 3,48783 | 274
6 | 218 | 46,7 | 4,670317 | 1184
9 | 283,2 | 54,4 | 5,207954 | 2099
12 | 293,4 | 60,6 | 4,841523 | 1429
24 | 327,2 | 78,7 | 4,158793 | 653

## Slide 29: Diagramma di severità di evento Metodo Patched Kriging

## Slide 30: Metodo VAPI Sardegna 1998 modificato d<1h
d [h] | h [mm] | [mm] | KToss | T [anni]
0,25 | 23,8 | 10,2 | 2,327739 | 239
0,5 | 33,6 | 15,8 | 2,123479 | 49
0,75 | 42 | 20,4 | 2,055989 | 32
1 | 54 | 24,5 | 2,20523 | 38
3 | 125,4 | 38,7 | 3,23813 | 240
6 | 218 | 51,7 | 4,215589 | 1235
9 | 283,2 | 61,2 | 4,624094 | 2239
12 | 293,4 | 69,1 | 4,248805 | 1068
24 | 327,2 | 92,2 | 3,548338 | 272
d [h] | h [mm] |  | KToss | T [anni]
0,25 | 23,8 | 10,2 | 2,327739 | 239
0,5 | 33,6 | 15,8 | 2,123479 | 49
0,75 | 42 | 20,4 | 2,055989 | 32
1 | 54 | 24,5 | 2,20523 | 38
3 | 125,4 | 38,7 | 3,23813 | 240
6 | 218 | 51,7 | 4,215589 | 1235
9 | 283,2 | 61,2 | 4,624094 | 2239
12 | 293,4 | 69,1 | 4,248805 | 1068
24 | 327,2 | 92,2 | 3,548338 | 272

## Slide 31: Diagramma di severità di evento Metodo VAPI Sardegna 1998 modificato d<1h

## Slide 32: Metodo GEV geostatistico modificato d<1h
d [h] | h [mm] | [mm] | KToss | T [anni]
0,25 | 23,8 | 11,7 | 2,033329 | 44
0,5 | 33,6 | 16,7 | 2,009073 | 31
0,75 | 42 | 20,6 | 2,038222 | 29
1 | 54 | 23,9 | 2,259831 | 42
3 | 125,4 | 34,8 | 3,608377 | 373
6 | 218 | 44 | 4,952664 | 2363
9 | 283,2 | 50,5 | 5,603247 | 5314
12 | 293,4 | 55,8 | 5,262723 | 2831
24 | 327,2 | 70,6 | 4,63374 | 974
d [h] | h [mm] |  | KToss | T [anni]
0,25 | 23,8 | 11,7 | 2,033329 | 44
0,5 | 33,6 | 16,7 | 2,009073 | 31
0,75 | 42 | 20,6 | 2,038222 | 29
1 | 54 | 23,9 | 2,259831 | 42
3 | 125,4 | 34,8 | 3,608377 | 373
6 | 218 | 44 | 4,952664 | 2363
9 | 283,2 | 50,5 | 5,603247 | 5314
12 | 293,4 | 55,8 | 5,262723 | 2831
24 | 327,2 | 70,6 | 4,63374 | 974

## Slide 33: Diagramma di severità di evento Metodo GEV geostatistico modificato d<1h

## Slide 34: 3 Regional methods
Critical rainfall (d=tc)
Antecedent precipitation

## Slide 35: Update 3 (to the UPH 21): How to combine T of the runoff coefficient and the T of precipitation?
T1
T2
Claps, Mazzoglio, Deidda, Volpini, Perucca and … ?. .